## Slide 1: Biomethane from municipal organic waste as fuel for waste-collecting vehicles
Wilhelm Winkelmann, Berliner Stadtreinigung
01/24/2022

## Slide 2: Fermentation of organic waste: Additional benefit from linked cycles
1. Disposal
of organic waste
(waste bins)
2. Collecting
of organic waste
(waste bins)
3. Waste treatment
processing and
fermentation
4. Preparation
of biogas and
feeding into
natural gas grid
5. Refueling
BSR vehicle fleet
4. Preparation
of digestate
(compost, liquid fertilizer)
5. Delivery
gardening &
landscaping
companies;
agriculture
6. Agricultural
products
e.g. plants, corn

## Slide 3: Development of organic waste in Berlin Berlin without Brandenburg
Organic
matter
Fallen leaves (loose + in bags)
Tree & shrub brashings
Christmas trees

## Slide 4: Organic waste - Ways of treatment
Organic Waste |  |  | 
 | - hardly fermentable - |  | - fermentable -
 | non-compostable | compostable | 
 | wood fallen leaves | organic waste tree- and shrub brashings fallen leaves | organic waste leftovers e.g. canteen
recycling | incineration | composting | fermentation

## Slide 5: Concept of organic waste fermentation
organic matter
digestate
- liquid
- solid
hydrolysis
propionic acid
acetic acid
methane+CO2
substrate intake
saliva
rumen
omasum
abomasum
small/large intestine

## Slide 6: Possibilities of using biogas
standard | filling into public – natural gas grid |  | biofuel | biogas pipeline (micro gas grid)
biogenous fermentable waste |  |  |  | 
production of biogas |  |  |  | 
 | biogas-processing |  |  | biogas pipeline
 | biomethane into grid |  | biomethane filling station | 
combined heat and power (CHP) electricity heat | withdrawal from grid |  | biogas vehicle fleet | combined heat and power (CHP) electricity heat
 | other consumers | BSR methane filling stations |  | 
 |  | BSR vehicle fleet |  | 

## Slide 7: Key figures 2021
    Input: 75,000 Mg/a organic waste from households
    Area: 2.7 ha
    Employees: 16
    Exhaust air: 40,000 m3/h
    Production of raw biogas: 103 m3/Mg Input with 56% CH4
    Annual production of raw biogas: ~ 6 Mio. m3/a
    Production of biomethane: ~ 3 Mio. m3/a
    Net production of energy: ~ 31 Mio. kWh/a
    Substitution of diesel fuel: ~ 2,5 Mio. liters/a
    Output solid aerated fermentation residue: 20,000 Mg/a (c-sequestration, compost)
    Output liquid digestate : 40,000 Mg/a (liquid fertilizer)
    CO2-reduction potential: ~ 13,800 Mg CO2/a from substitution of fuel and c-sequestration
    or 185 kg CO2/Mg Input

## Slide 8: Biomethane used as fuel
    3 high-performance gas stations for our
    vehicle fleet
    165 waste collection vehicles run on
    biomethane
    (= 50 % of waste collecting vehicle fleet)
    467,000 Mg waste* from
    1.97 Mio. private households** of the city of Berlin are being collected and transported per year …
    with no negative effect on our climate
* residual waste, organic waste (brown bin); ** www.destatis.de, survey 2020

## Slide 9
From waste to value

## Slide 10: Proceeds from recycling provide a significant contribution to securing steady fees
Steam:
(incinearation plant Ruhleben)
Scrap metal (FE and NF):
(incinearation plant Ruhleben, treatment of bulky waste, recycling centers)
Other:
(e.g. old clothes, recyclables)
Biomethane:
(fermentation plant for organic waste)
Paper:
(recycling centers)
Wood:
(treatment of bulky waste, recycling centers)
2.3%
2.1%
0.5%
0.2%
0.4%
6.0%
0.5%
Reduction
of fees
status: 2020

## Slide 11: Biogas plant in Berlin: Sources of proceeds
    Using the natural gas grid allows:
Selling of biomethane
Delivery of gas to our fleet of collecting vehicles (gas stations)
Delivery of gas to CHP plant
Fuel quota trading
External revenue
(Advanced fuels)
Internal transfer price
Internal transfer price
Quota trading
38. BImSchV / RED II
approx. 2.3 GWh/a
approx. 26 GWh/a
2.2 GWh/a
electricity and heat
approx. 26 GWh/a
or approx. 6 Tsd. Mg CO2-Äq.
price development

## Slide 12: Conclusion and Prospect
    The high level of contributing households to the organic waste collection reduces costs of the collection system
    Chosen concept helps to reduce emissions of logistics (CO2, noise, PM 10-particles)
    The recycling of digestate improves the humus balance and reduces the need for artificial fertilizers
    Prices for utilization of compost and liquid digestate increase because of aggravating legal developments
    Secured access to the public natural gas grid by law is essential (storage function of grid)
    Political strategies for the transport sector are changing; the legislator pushes the development and usage of e-fuels (fuels from renewable resources). But Daimler Comp. stops production of CNG-trucks for waste collection
    Little extra money (increasing) from selling quotas for renewable fuels (BioKraftQuG / RED II)
    Video about this concept: https://www.bsr.de/biogasanlage-22250.php

## Slide 13: Thank you for your attention!

## Slide 14: BACKUP
14

## Slide 15: A big city can be supplied with electricity and heat from the energy in Berlin's waste (Status 04.2021)
approx. 42 GWh electricity, approx. 21 GWh district heating
3 landfill sites
with CHP
2 mechan.-physic. stabilization system plants
processing of waste wood and bulky waste
steam
approx. 1.5 Mio. Mg/a
gas from landfill sites:
approx. 22 Mio. m3/a
substitute solid fuel:
approx. 187,000 Mg/a
substitute solid fuel:
approx. 60,000 Mg/a
approx. 210 GWh electricity
approx. 740 GWh
district heating
approx. 194 GWh electricity
approx. 70 GWh electricity
Covers need for electricity of approx. 12 % of average households of Berlin and the need for district heating of approx. 7.4% of households of Berlin with a district heating connection
15
fermentation plant for organic waste
biomethane: approx. 31,800 MWh/a
approx. 25,700 MWh for substitution of von Diesel fuel; approx. 2,200 MWh for generation of electricity and heat CHP
incineration plant Ruhleben